## Slide 1
ZHAW · BLOCKWEEK BIONICS 2026 · CHALLENGE 1
Discovering &
Abstracting
Twelve biological models for cooling a city, the mechanism behind each one, and what it would mean for Zurich.
MODELS FOUND
12
DE-SELECTED
4
FUNCTIONS COVERED
F1–F11
REFERENCE CITY
Zurich
Cooling the City — urban heat islands

## Slide 2
THE PHASE
What this step has to deliver
THE SPIRAL
Discovering has two halves. DISCOVER: find biological models and the evidence for them. ABSTRACT: turn each mechanism into a transferable design principle — without copying the organism's shape.
REQUIRED OUTPUT
At least three biological models, an explicit research path showing how they were found and why others were dropped, mechanisms explained in depth, and a clean separation of biological observation, abstracted principle and possible technical interpretation.
WHAT WE HAVE
Twelve models, each mapped to one of our functions F1–F11, plus four documented de-selections. The abstraction of every model is stated on its own slide, in the highlighted band.
"Do not stop at the organism. The mechanism is more important than the name." — Discovering lecture, slide 34
THE PHASE
02

## Slide 3
RESEARCH PATH
How we searched
BY FUNCTION, NOT BY ORGANISM
Every search started from a verb in our function list, never from an animal. "How does nature emit heat to the night sky?" — not "how does a termite mound work?"
THE TAXONOMY AS THE MAP
F1 reflect → Modify physical state: light/colour. F2 emit → Transform energy: thermal. F6–F8 water → Capture, Store and Distribute liquids. F9 is the exception: it is the pairing of Sense signals: temperature with Process signals: respond to signals.
FOUR SOURCE TYPES
AskNature strategies and innovations · the Genius of Biome report for the temperate broadleaf forest, which is Zurich's own biome · primary papers behind each claim · commercial products where the transfer has already been made.
Discovery is not evidence. AskNature and AI find candidates; the paper or the measurement is what we cite.
RESEARCH PATH
03

## Slide 4
BIOLOGIZED QUESTIONS
From our functions to questions for nature
PREVENTION — F1, F5
How does nature reflect intense sunlight without pigments that bleach and without a mirror finish? How does nature shade itself with its own geometry?
REMOVAL — F2, F3, F4
How does nature release heat to the night sky? How does nature hand heat to moving air? How does nature buffer a daily extreme instead of resisting it?
WATER AND REGULATION — F6–F9
How does nature capture, store and meter out scarce water so a reserve lasts a dry period? And the central one: how does nature make a response stronger when the load is stronger, without a controller?
The challenge brief asks a fourth question we should answer explicitly: what can we learn from desert organisms about passive cooling?
BIOLOGIZED QUESTIONS
04

## Slide 5
MODEL 01 · F2 · F3 REMOVAL
African elephant — ears
Loxodonta africana · dissipates body heat in hot, exposed habitat
ABSTRACTION
Transfer heat to a large surface and increase the airflow around it.
THE MECHANISM
Warm blood is carried from the body core into large, thin ears. The big, well-supplied surface lets heat escape to the air, and flapping raises the airflow across it.
WHAT IT MEANS FOR THE CITY
It separates where heat is picked up from where it is released. A canyon wall stores heat but cannot get rid of it; a dedicated, well-exposed surface can.
asknature.org/strategy/large-ears-aid-cooling/
05

## Slide 6
MODEL 02 · F3 REMOVAL
Elephant skin — sparse hairs
Micro-finned surface · heat transfer at low wind speed
ABSTRACTION
Add small protrusions to break the boundary layer and hand heat over to passing air.
THE MECHANISM
A thin layer of still air clings to any warm surface and insulates it. Sparse hairs reach through that boundary layer so moving air actually reaches the skin. Reported additional heat loss of up to 23 %.
WHAT IT MEANS FOR THE CITY
Street canyons have low wind speeds, so the insulating boundary layer is thick. Texture at millimetre scale on façades and pavements adds no material and no maintenance.
sites.nd.edu — biomechanics in the wild · asknature.org/strategy/small-leaves-buffer-insect-eggs-from-heat/
06

## Slide 7
MODEL 03 · F1 · F2 PREVENTION + REMOVAL
Tree bark
e.g. paperbark maple, Acer griseum · keeps the surface cool in sun
ABSTRACTION
Reflect the incoming energy, emit the stored energy, and use texture for shade and airflow.
THE MECHANISM
Bark reflects part of the incoming sunlight and emits thermal radiation efficiently. Rough, layered bark also shades itself, traps insulating air and improves convection.
WHAT IT MEANS FOR THE CITY
One surface doing prevention and removal at once — and bark is the closest natural analogue to what we are designing: a dead outer layer protecting a living structure behind it.
asknature.org/strategy/bark-keeps-surface-cool-under-the-sun/
07

## Slide 8
MODEL 04 · F5 · F3 · F2 PREVENTION + REMOVAL
Cactus ribs
Ribbed and barrel cacti · less overheating, less water loss
ABSTRACTION
Use folded or ribbed geometry for self-shading, more surface and better airflow.
THE MECHANISM
Peaks shade the troughs. The cooler air collecting in the troughs absorbs heat from the body, rises and is carried away, while the folds enlarge the radiating area and disturb the airflow.
WHAT IT MEANS FOR THE CITY
Costs no material, no water and no chemistry, and there is nothing to bleach or run out. The conflict is visible change on a protected façade — the feature size is the negotiable part.
asknature.org/strategy/shape-shades-and-enhances-heat-radiation/
08

## Slide 9
MODEL 05 · F9 · F2 SELF-REGULATION
Jackrabbit ears · elephant hot spots
Cooling by varying the transport, not the surface
ABSTRACTION
Regulate cooling by varying the transport to a radiating surface, and place that radiator only where the conditions are best.
THE MECHANISM
The jackrabbit widens or narrows the vessels in its thin ears; at around 30 °C air temperature the ears alone carry all its excess heat, and it costs no water. Elephants open small cooling windows scattered over the skin, as many as the heat requires.
WHAT IT MEANS FOR THE CITY
A wall at eye level barely sees the sky — that blocked view is the physical cause of the night-time heat island. A parapet two floors up sees it well. A loop driven by density differences needs no pump and strengthens as the temperature difference grows.
asknature.org/strategy/how-blood-flow-keeps-jackrabbits-cool/ · asknature.org/strategy/skin-fine-tunes-internal-temperature/
09

## Slide 10
MODEL 06 · F1 · F4 PREVENTION + STORAGE
Desert snail shell
Sphincterochila boissieri · survives ground heat up to 50 °C
ABSTRACTION
Reflect first — then decouple whatever still gets through, with a layer of air.
THE MECHANISM
The shell reflects about 90 % of visible light and about 95 % in the near infrared. When conditions get extreme the snail seals the opening with a calcified plate and withdraws, leaving a layer of air between itself and the hot ground.
WHAT IT MEANS FOR THE CITY
The 7 K a city is warmer at night is heat released from mass charged during the day. A reflective skin over a ventilated cavity stops the masonry charging in the first place — and that is a standard façade system, not an exotic one.
asknature.org/strategy/shell-protects-from-heat/
10

## Slide 11
MODEL 07 · F1 PREVENTION
Morpho butterfly wing
Brilliantly blue, with no blue pigment at all
ABSTRACTION
Separate what a surface looks like from what it does with heat.
THE MECHANISM
Transparent layers of chitin and air, a few hundred nanometres apart, diffract the light and recombine it so that some wavelengths cancel and others are reinforced. The colour is in the geometry, and because the structure is disordered it stays diffuse rather than mirror-like.
WHAT IT MEANS FOR THE CITY
About half the sun's energy arrives as invisible near infrared. A façade can keep the ochre of the old town and still reject the heat — which is what decides whether the measure is ever permitted, and it answers the glare objection too.
asknature.org/strategy/wing-scales-cause-light-to-diffract-and-interfere/
11

## Slide 12
MODEL 08 · F9 · F8 SELF-REGULATION
Leaf stomata
Cooling regulated by the opening itself
ABSTRACTION
Build the control into the opening, so the escape route widens as the load rises.
THE MECHANISM
Two guard cells swell and shrink with their water content and so open and close the pore. The water is pulled up from the roots by the evaporation itself — there is no pump anywhere. The leaf cools itself by more than 10 K.
WHAT IT MEANS FOR THE CITY
Evaporation is the only mechanism here that cools the air people actually breathe, rather than only the surface they walk past. The binding limit is water: during a heat wave it does not rain.
Genius of Biome, pp. 62–65 — Day 2 course material
12

## Slide 13
MODEL 09 · F7 · F8 WATER PATH
Camel fur and sweat glands
Built at MIT as a hydrogel under an aerogel
ABSTRACTION
Cut the heat load first, then spend a little water on what is left — and insulate the wet layer so the reserve lasts.
THE MECHANISM
A hydrogel layer evaporates like a sweat gland, underneath an aerogel layer that blocks incoming heat but lets the vapour through, like fur. The pair held a sample 7 K below ambient for 200 hours — five times longer than the hydrogel alone.
WHAT IT MEANS FOR THE CITY
Zurich has ample rain over a year and almost none during a heat wave, so our problem is storage and metering, not collection. It also rules out fog harvesting: fog here is a winter phenomenon.
asknature.org/innovation/passive-cooling-system-inspired-by-camels/
13

## Slide 14
MODEL 10 · F5 · F9 PREVENTION + SELF-REGULATION
Pine cone scales
Dead tissue, moved entirely by the weather
ABSTRACTION
Make moving parts from two layers that respond differently, and let the environment do the actuating.
THE MECHANISM
Each scale is two bonded layers that swell differently with moisture, so the scale bends. Already built twice: HygroSkin, whose wooden apertures are shut at 30 % humidity and open at 75 %, and thermobimetal shutters that curl in the sun — explicitly with no energy and no controls.
WHAT IT MEANS FOR THE CITY
A shade takes the sun off the person, not just off the wall. And by retracting when it cools it leaves the night sky open, which fixed shading does not. The risk is wind: a thermal actuator cannot feel a storm.
asknature.org/strategy/pine-cones-open-and-close-in-response-to-weather/
14

## Slide 15
MODEL 11 · F9 SELF-REGULATION
Honeybee fanning thresholds
A colony holds 36 °C with no central control
ABSTRACTION
Spread many binary elements across a range of trigger points, and the sum responds continuously.
THE MECHANISM
Every worker starts fanning at a slightly different temperature, and the spread is genetic — one queen, many fathers, therefore many thresholds in one nest. As it warms, a few bees fan, then more, then many.
WHAT IT MEANS FOR THE CITY
This answers the standard objection to switching materials, that they are all-or-nothing. Build whatever we build as many small units with different trigger temperatures, and the response grows through the afternoon instead of snapping on.
asknature.org/strategy/varying-response-thresholds-aid-hive-thermoregulation/
15

## Slide 16
MODEL 12 · F10 · F11 SUPPORTING
Lichen surface
Lecanora conizaeoides · waterproof and breathable at once
ABSTRACTION
Use geometry rather than chemistry to shed water and stay clean.
THE MECHANISM
Roughness at several size scales keeps droplets perched on the peaks so they roll off, while the channels between them are coated to stay dry and still let air through to the algae inside. Dirt and biofilm find almost nothing to hold on to.
WHAT IT MEANS FOR THE CITY
The city names soiling as the specific weakness of bright envelopes. A lotus-effect façade paint has done this since 1999 without biocide — which matters twice over if we collect that run-off and evaporate it at head height.
Genius of Biome, pp. 41–44 · asknature.org/innovation/paint-inspired-by-lotus-leaves-creates-self-cleaning-and-antifouling-surfaces/
16

## Slide 17
DE-SELECTION
What we looked at and left out
THE TERMITE MOUND
The Eastgate building that made it famous uses fans, and the chimney explanation is contested in the literature (Turner 2008). It is not the passive system it is sold as.
FOG HARVESTING — THE NAMIB BEETLE
The most-cited water model in biomimicry, and wrong for our climate: Zurich's fog is a winter phenomenon, and during a heat wave there is neither rain nor fog.
GREEN FAÇADES · GAZELLE CAROTID RETE · TENREC DORMANCY
Greening is already the city's own measures HA 09 and HA 10, and it needs the most water exactly when we have the least. The other two are internal physiology and behaviour — a wall has neither.
The criterion throughout: it has to be passive, survive frost and UV for twenty years, and live in a surface.
DE-SELECTION
17

## Slide 18
SYNTHESIS
What the twelve models have in common
ONE PRINCIPLE, FOUND THREE TIMES
Bees vary their thresholds, elephants vary how many cooling windows are open, a deployable shade varies how much area is spread. All three regulate how MANY elements act — not how strongly each one acts. That is our answer to F9.
PREVENTION IS THE SMALLER HALF
Models 3, 4, 6 and 7 stop heat arriving. Only 1, 2, 5, 8, 9 and 10 get heat out again — and the urban heat island is 1–2 K by day against up to 7 K at night. The night belongs to the removal side.
STRUCTURES TRANSFER BETTER THAN PROCESSES
Most cooling in nature is metabolism or behaviour, and a façade has neither. The two models that transfer most directly — the snail shell and the cactus rib — are the two that are structures rather than processes.
SYNTHESIS
18

## Slide 19
NEXT
From principles to concepts
THE MORPHOLOGICAL MATRIX
Rows are our functions, columns are the abstracted principles on these slides. Reflect: structural colour · ribbed geometry · reflective skin with an air gap. Remove: passive loop to a roof radiator · boundary-layer texture · metered evaporation.
THEN TWO TECHNICALLY DISTINCT CONCEPTS
Not two cosmetic variants. Each with an annotated drawing, an Engineering Canvas, and two or three critical questions of the form "what must be true for this to work?"
THE THREE QUESTIONS WE ALREADY KNOW WE HAVE TO ANSWER
Can a passive loop survive a Swiss winter? Can a shading element be furled by wind without a controller? And can a switching material be made with a deliberate spread of trigger temperatures?
NEXT
19